## Slide 1: Canadian Satellite Design Challenge CSDC-4 Critical Design Review
Queen’s Space Engineering Team (QSET)
Bryan Little, Matthew Bowen, James Xie
Sept. 21, 2017

## Slide 2: Presentation Outline
Mission Overview
Spacecraft Overview
  Payload(s) Description
  Structure
  Thermal
  Power
  Attitude & Orbit Determination & Control
  Communications
  Command & Data Handling
Assembly, Integration, and Test
Programme Management
Concept of Operations
Educational Outreach
Summary

## Slide 3: Mission Overview

## Slide 4: Mission Summary
Problem
Experiment
Subject space-grade materials to orbital decay
Measure spectral reflectance change over time
Result
Material reflectance behavior in space is now known
SSA community determines what each object is
Must understand material spectral changes over time
Orbital object identification using their spectra
PRIMARY MISSION
Problem
Experiment
Mount green & red LEDs to external panels
Result
CCD camera used to determine wavelength of LED or;
Visual communication
Satellite cluster identification
Flash either green or red LEDs while over ground station
Receive low-bandwidth data from Morse code blinking
SECONDARY MISSION

## Slide 5: Spacecraft Summary
Nadir over Kingston
Spectral Slot
Solar cells
X+
Z+
Y+
Antennas
LEDs

## Slide 6: Mission Ground Track and Ground Station Access (1/2)
Notes: July 1st, 00h00 to July 2nd, 00h00

## Slide 7: Mission Ground Track and Ground Station Access (2/2)
Ground Station:
  Royal Military College of Canada SSRL
  44°14’1.97” N, 76°28’3.02” W
Passes per day:
  Minimum: 6
  Average: 6.8
Daily contact time:
  Minimum: 58.4 minutes
  Average: 64. 6 minutes

## Slide 8: Changes to Payload 1 Since PDR – Original Design

## Slide 9: Changes to Payload 1 Since PDR – Updated Design
Aspheric Lens
Notes: LED banks substituted for quartz tungsten-halogen lamp
  Simpler electronics (less crowding, more throughput), more uniform spectra
Increased samples from 2 to 3 in addition to reference
Change of observation angle from 10º to 60º
  Increased exposure area and better protection of optics
Combination of fiber optic and free space assembly
  Reduction of complexity and error
Overall refinement of design to match ground-based lab settings

## Slide 10: Spacecraft Overview

## Slide 11: System Level Configuration Trade Selection
Build
  Chosen to design subsystems in areas where members possess expertise
  Team involves graduate students with specialized skill sets
    FEM, Mechanical Design Optimization, RF design
  Parts manufactured in-house will undergo rigorous qualification
    Spectrometer system (TRIUMF), ACDS (Engineering Physics Department), Structure (Vibration and Noise Laboratory)
Buy
  Subsystems requiring extensive background knowledge to build from the ground up
  Preference given to flight heritage components

## Slide 12: System Level Configuration Trade Selection
Structure
  Team has strong background in mechanical design
  Freedom to customize structure to accommodate unconventional payload
  Fraction of the cost of a ready-made structure
  Discounted shop rates (for parts requiring specialized milling) and raw material costs

## Slide 13: System Level Configuration Trade Selection
Thermal
  Sponsorship discount from company producing MLI kits
  Insulation requirement being evaluated; dependent on outcome of thermal simulations
  If purchased, implementation would be planned and applied by thermal team

## Slide 14: System Level Configuration Trade Selection
ADC
  Neither payload requires active control
  Many theses/journal papers detailing research and application of passive control systems
    Position and layout of magnets/ hysteresis rods
  Passive attitude control cannot be directly purchased regardless

## Slide 15: System Level Configuration Trade Selection
ADC (cont’d)
  Passive system saves cost of actuators and controller (thousand dollar range)
  Possess calibration equipment to measure and tune response of permanent magnets and dampers
  Design of sun-sensor system and CDH programs to determine acceptable attitude

## Slide 16: System Level Configuration Trade Selection
Power System
  Have background to configure and tune final product to the needs of the satellite bus/payloads
  Do not possess resources to fabricate PCBs in house
    Especially with regards to validation for spaceflight
    E.g, Conformal coating, verified fail-safe operation

## Slide 17: System Level Configuration Trade Selection
Power System
Supplier | Part Name | Native Cost | Cost (CAD) | Notes
NanoAvionics | EPS | 3000 EUR | 4505.00 | Includes batteries, coarse sun sensing, Price in Euro (Additional levys, duties)
ASTERLabs | NanoPowerP31uX | 4600 USD | 5808.00 | No batteries, Price in USD

## Slide 18: System Level Configuration Trade Selection
Communication System and Antenna
  Purchasing antenna and communications board from same company ensures compatibility
  Eliminating subsystem design in these areas
    Strictly configuration, testing, and integration

## Slide 19: System Level Configuration Trade Selection
Communication System
Supplier | Part Name | Native Cost | Cost (CAD) | Notes
NanoAvionics | UHF Digital Radio SatCOM UHF | 4500.00 Euro | 6758.00 | Price in Euro
ASTERLabs | NanoCom AX100-U | 7250.00 USD | 9155.00 | Price in USD

## Slide 20: System Level Configuration Trade Selection
Antenna
Supplier | Part Name | Native Cost | Cost (CAD) | Notes
NanoAvionics | UHF/VHF Antenna | 2500 | 3754.61 | Price in Euro
ASTERLabs | NanoCom ANT430 | 6250 | 7892.25 | Price in USD

## Slide 21: System Level Configuration Trade Selection
Command and Data Handling
  Decision to purchase generic embedded system
    Not specifically designed for Nanosatellites, but robust enough to handle harsh environment
    Large cost reduction over satellite part provider
    Chosen board, accessories, and support received free of charge from Technologic Systems (TS-7600)
    Hard/Software capable of handling payloads, network routing, data I/O, subsystem interfacing

## Slide 22: System Level Configuration Trade Selection
Command and Data Handling
Features
  1.2W Max, Watchdog timer, 8 Serial Ports, SPI, I2C, CAN, RTC, 10/100 Ethernet, microSD socket
Name | CPU | RAM | Storage | DAC | Kernel
TS-7600 | 454MHZ, ARM | 256MB | 8MB | 55 DIO 4 A2D | Linux v2.6.35

## Slide 23: Physical Layout
EPS/Batteries
Collimating Lenses
OBC
Sample Material
Spectrometer
Transceiver
Tungsten Halogen Bulbs
Antennas
Sample Stage

## Slide 24: Payloads

## Slide 25: Payload #1: Material Degradation in Space
CoSMOSAT monitors time-dependent degradation of common spacecraft materials via reflectance spectra
  Augments ground-based data to identify the composition, orientation, and age of debris [P1, P2]
  Reflection spectroscopy is cost-effective
  Addresses knowledge gap of how material reflectance changes over time in space environments [P1]
Ground observations are impractical to generate data
  Requires fine control of reflection geometry, age knowledge, and has limitations of telescope usage time and weather [P1]
  Cannot distinguish individual materials
  Lab experiments cannot efficiently and accurately recreate long exposure to the complex LEO environments [P1]

## Slide 26: Payload #1: Material Degradation in Space (cont.)
Payload compresses large-scale lab experiment into a 1U compartment
  Unique experiment provides first time-evolving data on material degradation [P1]
  Extends existing data and augments ground-based observations, allowing them to be used in space applications
Payload is a joint project between Queen’s University and Royal Military College, and builds off of Major Donald Bédard’s work.
  Collected data will be used by researchers and the space industry in space situational awareness (SSA) [P1]
  Provides more granularity than the NASA Long-Duration Exposure Facility (LDEF) experiments [P1]
Notes:   What is new or innovative about this payload experiment?

## Slide 27: Payload #1: Physical Characteristics
Physical Size | Total Mass | Data Throughput
1400 cm3 | 870 g | 125 kB/day

## Slide 28: Payload #1: Performance Characteristics
Record spectra of 3 samples exposed to the space environment and one reference
Spectra range of 400–1100 nm @ 2.35 nm resolution [P3]
Sampling in eclipse when light level drops below 1% reference signal strength
No requirements on orbital position or attitude.
  In eclipse/sufficient darkness, on-board lighting will be used
  Otherwise, the sun may act as a light source, with illumination geometry calculated on the ground via attitude data [P1]
Notes: Objective coverage characteristics & statistics
  E.g., Earth imagery in km2/day
What attitude and orbit position accuracy does your payload need? What happens if it doesn’t get that?

## Slide 29: Payload #2 – Satellite Identification via VLC (LEDSAT)
Clusters of nano-satellites can be difficult to identify
Externally-mounted LEDs may be used
Satellite-to-ground Visual Light Communication (VLC)
  Upon deployment, LEDs are initiated when over Kingston during eclipse
  Astronomical camera with CCD attached to RMC telescope for wavelength identification
Telescope, CCD with John-Cousins Filters

## Slide 30: Payload #2 – LEDSAT (cont.)
Why should it be put into space?
  Identification of nano-satellites without operator communication
  Can LED wavelength be determined from 400-1200 km away through Earth’s atmosphere? How do LEDs degrade under radiation over time?
What is innovative about this payload?
  Identification using both LED wavelength and blinking schemes
  Ability to function while tumbling and stabilized
Partners
  RMC is initiating a project to standardize external LEDs for CubeSats
  May also be used for educational outreach

## Slide 31: Payload #2 - LEDSAT: Characteristics
-z
6 green LEDs & 6 red LEDs on +X,+Y,-X,-Y,-Z faces

## Slide 32: Payload #2 - LEDSAT: Characteristics
x48
 | Wavelength (nm) | Forward Current (A) | Forward Voltage (V) | Luminous Flux (lm) | Radiant Flux (W) | (FWHM) | Operating Temperature (°C)
Red | 620-635 | 0.35 | 3.00 | 56.8 | 0.3737 | 62.5 | -40/+80
Green | 513-543 | 0.35 | 3.35 | 130 | 0.2440 | 60 | -40/+80
Dimensions in mm

## Slide 33: References
[P1] | D. Bedard, A. Willison, P. Seitzer and P. Somers, "In-Situ VIS/NIR Measurements of Space Environment Effects on Spacecraft Surfaces," in AMOS Technologies Conference, Maui, Hawai'i, 2016.
[P2] | Donald Bedard, Gregg A. Wade, and Kira Abercromby, “Laboratory Characterization of Homogenous Spacecraft Materials,” Journal of Spacecraft and Rockets, vol. 52, no. 4, pp. 1038–1054, 2015.
[P3] | Avantes BV, “AvaSpec-Mini.” Avantes BV, 2017.
[P4] | Donald Bedard and Martin Levesque, “Analysis of the CanX-1 Engineering Model Spectral Reflectance Measurements,” Journal of Spacecraft and Rockets, vol. 51, no. 5, pp. 1492–1504, 2014.
[P5] | T. Kiuchi and K. Ikeuchi, "Determining the Surface Roughness and Shape of Specular Diffuse Lobe Objects Using Photometric Sampling Device," IAPR Workshop on Machine Vision Applications , pp. 175-178, 7-9 December 1992.
[P6] | Thorlabs Inc., “Quartz Tungsten-Halogen Lamp.” Thorlabs Inc., 2017.
[P7] | S. K. Miller, "Degradation of Spacecraft Materials in the Space Environment," MRS Bulletin, vol. 35, January 2010.

## Slide 34: Spacecraft Structure

## Slide 35: Spacecraft Structural Drawings
All Dimensions
In mm

## Slide 36: Structural
Involved
Start
[DIETR-0320] Launch Vibration Test
Center of Mass:
X-Axis:
Y-Axis:
Z-Axis:
(With respect to center of total structure)
Moments of Inertia ():

## Slide 37: Structural
Involved
Start
[DIETR-0320] Launch Vibration Test
Mesh Size:
Nodes:
Elements:

## Slide 38: Structural – Frame Material
Involved
Start
 | Main Structure | Inner Structure
Material | 7075-T6 Plate | 7075-T6 Plate
Finish | Type III Hard Anodize | Type II Anodize
Dimension |  | 
Mass |  | 
 | Main Structure | Inner Structure
Material | 7075-T6 Plate | 7075-T6 Plate
Finish | Type III Hard Anodize | Type II Anodize
Dimension |  | 
Mass |  | 

## Slide 39: Structural – Spacecraft Static Analysis
Involved
Start
G-Study:
X-Axis:
Y-Axis:
Z-Axis:
Maximum Deformation:
Rib 2:
[DIETR-0310] Launch Quasi-static Acceleration Test

## Slide 40: Structural – Spacecraft Static Analysis (cont.)
Involved
Start
Maximum Stress:
Rib 4:
[DIETR-0310] Launch Quasi-static Acceleration Test
G-Study:
X-Axis:
Y-Axis:
Z-Axis:

## Slide 41: Structural – Safety Factor
Involved
Start
S
[DIETR-0310] Launch Quasi-static Acceleration Test
G-Study:
X-Axis:
Y-Axis:
Z-Axis:

## Slide 42: Structural – Normal Modes Analysis
Involved
Start
Modal-Study:
Mode 1:
[DIETR-0200] Fundamental Frequency

## Slide 43: Structural
Involved
Start
Modal-Study:
Mode 1:
[DIETR-0200] Fundamental Frequency

## Slide 44: Structural – Normal Modes Analysis (cont.)
Involved
Start
Modal-Study: First 50 Modes of vibration
[DIETR-0200] Fundamental Frequency

## Slide 45: Structural – Launch Vibration Study
Involved
Start
Launch Vibration-Study: X-Axis
Maximum Deformation:
Rib 2:
[DIETR-0320] Launch Vibration Test

## Slide 46: Structural – Launch Vibration Study (cont.)
Involved
Start
Launch Vibration-Study: Y-Axis
Maximum Deformation:
Rib 1:
[DIETR-0320] Launch Vibration Test

## Slide 47: Structural – Launch Vibration Study (cont.)
Involved
Start
Launch Vibration-Study: Z-Axis
Maximum Deformation:
Rib 1:
[DIETR-0320] Launch Vibration Test

## Slide 48: Mass Budget

## Slide 49: Thermal Analysis

## Slide 50: Thermal Analysis
Direct Solar
Albedo
Earth IR
Internal Sources | Sinks
Batteries/EPS | Primary/Secondary Structure
CDH/Transceiver | Radiation to space
Spectrometer | 
Tungsten Halogen Bulbs | 
Panel LEDs | 

## Slide 51: Thermal Analysis: Set-Up
Spectrometer
10 W Halogen Bulbs
EPS
Lens Trio
OBC
Transceiver
Notes: Mention neglected: magnets, LEDs

## Slide 52: Thermal Analysis: Set-Up (Cont.)
Conduction and radiation (Monte Carlo Ray-Tracing)
Tetrahedron mesh
Can simulate any beta angle, solar flux, Earth IR, etc.
Conduction and radiation contacts between internal components inner secondary structure
EPS/Batteries | -40°C / +85°C
Spectrometer | 0°C / 50°C
OBC | -20°C / 70°C
Transceiver | -40°C / +85°C

## Slide 53: Thermal Analysis: Case Study
Source | Payload 1 Case | Hot Case | Cold Case
Sun | 0 W/m² | 1428 W/m² | 0 W/m²
Albedo | 0 | 0.37 | 0
Earth IR | 150 W/m² | 350 W/m² | 150 W/m²
Beta Angle | - | 0° | -
TS-7600 | 0.5 W | 1.2 W | 0.25 W
EPS | 0.16 W | 0.16 mW | 0.16 W
Transceiver | 0 W | 2.805 W | 0 W
Spectrometre | 3.75 | 0 W | 0 W
Halogen Bulbs | 10 W | 0 W | 0 W

## Slide 54: Thermal Analysis: Steady-State Payload 1 Mode

## Slide 55: Thermal Analysis: Steady-State Hot Case

## Slide 56: Thermal Analysis: Steady-State Cold Case
Notes: If we are in a very cold orbit, and turn on the halogen lamps, the gradient could be detrimental

## Slide 57: Thermal Analysis: Temperature Margins
Component | Payload 1 Case | Hot Case | Cold Case
Spectrometre | 7°C | +13°C | -65°C
Transceiver | 12°C | 16°C | 8°C
Batteries | -3°C | 29°C | -7°C
TS-7600 | 31°C | 0°C | 9°C
MLI may be required for spectrometre

## Slide 58: Power Sub-system

## Slide 59: Power Sub-system: Block Diagram

## Slide 60: Power Sub-system: Block Diagram

## Slide 61: Power Sub-system: Power Generation
PV info:
+X,-X,+Y faces custom panel: 6X Azur cells [6S1P: 14.1V, 0.47A] (30%)
-Y face custom panel: 4X Azur cells [4S1P: 9.4V, 0.47A] (30%)
+Z face custom panel w. 2X Azur cells [2S1P: 4.7V, 0.47A] (30%)
Battery info:
2 li-ion 18650 cells
3.7V each or 7.4V open circuit
3200mAh or 23,000 Wh capacity
Max unregulated output: 25W (at 7.4V)
Max regulated output: 20W
Largest DOD: 78%
-Physical Specs: 18.6(D) x 65.2(L) mm cylinder
-2x this for total package size ~38(W)x19(H)x65(L)mm
Orbit info:
LEO ISS orbit
Orbit length (hrs): 1.54
Sunlight hours per orbit: 0.96
Orbit Average Power: 4.3W
Power Regulation:
4 regulated, OC protected buses:
3.3V
5V
2X 2.7V-18V (configurable)
Configure to 12V for Payload1
Power distribution through PC104 connector

## Slide 62: Power Sub-system: Power Budget

## Slide 63: Attitude & Orbit Determination & Control (AODC)

## Slide 64: ADCS Papers
Rawashdeh S., (2010) “PASSIVE ATTITUDE STABILIZATION FOR SMALL SATELLITES”
B. M. Menges., C. A. Guadiamos, E. K. Lewis., "Dynamic Modeling of MicroSatellite Spartnik’s Attitude." 1998. 36th AIAA Aerospace Sciences Meeting and Exhibit
Tanaka T., (2015), “Overview and Operations of CubeSat FITSAT-1 (NIWAKA) ”
Virk R., (2012), "Modular Sun Sensor System for Orbital Attitude Determination“
Gerdhart, D. T., (2014), “Small Satellite Passive Magnetic Attitude Control”
A. Farrahi, A. Sanz-Andrés, (2013), "Efficiency of Hysteresis Rods in Small Spacecraft Attitude Stabilization”
N. Nakaya, K. Konoue, H. Sawada, et al., (2003), “Tokyo Tech CubeSat: CUTE-I - Design & Development of Flight Model and Future Plan”

## Slide 65: ADCS Overview
Pointing Accuracy
  Preferred orientation for COSMOSat -Z face towards Earth
  LEDSAT must have array pointed towards Kingston when overhead (44.23 latitude)
  LED array has a spread of 120°; 60° desired
MATLAB
  Working to replicate results from Rawashdeh (2010), Menges (1998) and Gerdhart (2014)
  Implement EOM to simulate de-tumbling response and orbital stability
Rawashdeh S,(2010) “PASSIVE ATTITUDE STABILIZATION FOR SMALL SATELLITES”
B. M. Menges, C. A. Guadiamos, E. K. Lewis., "Dynamic Modeling of MicroSatellite Spartnik’s Attitude." 1998. 36th AIAA Aerospace Sciences Meeting and Exhibit

## Slide 66: ADCS Overview
Attitude Sensors
  Sun sensing: Coarse (Solar Panel), Fine (Custom enclosed photodetector array)
  Triaxial MEMS Gyroscope:
    Drift error accumulates over time
  Magnetometers: Verify ACS, attitude from external field
Attitude Control
  Array of high strength magnets will provide passive control
  Hysteresis rods damp out any off-axis rotation
  De-tumbling operation requires no computational effort

## Slide 67: Modelling Tools
Can estimate current and future attitude near steady state, updating ground model with telemetry
ADCS models in development (MATLAB) to evaluate design
Planned torque models:
  Hysteresis material
  Magnetic material
  Aero torque
  Gravity gradient

## Slide 68: ADCS Control System
Dynamic attitude
  Attitude is a function of instantaneous orbit position and associated magnetic field lines
  During Kingston flyover, magnetic vector pointed westward and towards earth’s surface
  Near critical damping to prevent overshoot
N
S

## Slide 69: Attitude Sensor #1
Gyroscope: ST L3GD20
  Difficult to measure such low rotation rates, useful during the detumbling phase
    Digital zero-rate level >10 dps; other sensors offer ±1 dps
  Drifts over time as error accumulates
  Failure does not significantly affect design goals
  Gyroscopes used previously in CubeSat designs (CUTE-I, 2003)
Notes: Image: CUTE-I sensor board

## Slide 70: Attitude Sensor #2
Custom Sun Sensor
  Photodiode array with pinhole
  Expected accuracy of roughly ±0.3°
  Most consistent system, only works for half the orbital period
  Updated infrequently due to heating requirements
  Albedo of Earth and Moon may produce confusing results
  Requires sensor to be an side facing the sun at max ±45° range
  Failure significantly reduces AD accuracy

## Slide 71: Attitude Sensor #3
Magnetometer: MAG3110
  Requires calibration to reduce hysteresis rod and permanent magnet effects
  Verify performance of passive system
Testing
  Helmholtz cage planned to calibrate
  sensors and test passive system
  Rotation platform used to demonstrate
  damping and alignment ability
  Image: Gerdhart, D. T., (2014), “Small Satellite Passive Magnetic Attitude Control”

## Slide 72: Attitude Determination Truth Table
Gyroscope | Magnetometer | Sun Sensor | Overall accuracy (deg)
✔ | ✔ | ✔ | 1
✘ | ✔ | ✔ | 2
✘ | ✘ | ✔ | 1 or N/A
✔ | ✘ | ✔ | 1 or 10
✔ | ✘ | ✘ | N/A
✔ | ✔ | ✘ | 4
✘ | ✔ | ✘ | 5
✘ | ✘ | ✘ | N/A

## Slide 73: Attitude Actuators
Permanent Magnets:
  Alnico-5 or neodymium cylindrical magnets placed along rail interior
  Total strength of 1.5 Am2 per end (magnetic moment)
    Based off of Rawashdeh paper, currently determining from our calculations
  Capable of tracking magnetic field within hours of deployment [1]
Failsafe
  Low probability of system not performing
    Attitude sensor input not necessary
    No power requirement
[1] Rawashdeh S,(2010) “PASSIVE ATTITUDE STABILIZATION FOR SMALL SATELLITES”
Notes: A. Farrahi, A. Sanz-Andrés, (2013), "Efficiency of Hysteresis Rods in Small Spacecraft Attitude Stabilization"

## Slide 74: Attitude Actuators
Hysteresis Rods
  Need sufficient material to damp rotation about Z-axis
  Too much can increase steady state error (lag) during orbits and interfere with LEDSAT operation
  8 rods/bars is typical to achieve damping in a wide variety of angles (TRANSIT-2A/1B, TNS-0/TEKh-42, KySat-1)
[1] Rawashdeh S,(2010) “PASSIVE ATTITUDE STABILIZATION FOR SMALL SATELLITES”
Material | HuMu80
Volume | 0.70 cm3
Coercivity | 1.59 A/m
Remanence | 0.35 Tesla
Saturation | 0.73 Tesla

## Slide 75: Communications Systems

## Slide 76: Communications System – Summary
  Uplink and downlink will be operating at 437 MHz
  Uplinks will be used to change the satellite mode
  Downlinks will be used to issue replies and download collected data
  All calculations for communications were based on using the Royal Military College of Canada's setup base station

## Slide 77: Communications System: Satellite Hardware
Nano Avionics UHF Antenna System and UHF Radio
  NA-RFS-G1-R2 and NA-UHF-G0-R0
9600 bit/s UART communications through radio
4 monopole antenna array matched to the radio
Images taken from Nano Avionics datasheets

## Slide 78: Communications System: Base Station Hardware
RMC a dual polarity Yagi-Uda antenna with 15dBi of gain and tracking
75W of transmit power
9600 bps transceiver

## Slide 79: Communications: Link Budgets

## Slide 80: Communications: Data Sources – Deployment Mode

## Slide 81: Communications: Data Sources – Default Mode

## Slide 82: Communications: Data Sources – Communication Mode

## Slide 83: Communications: Data Sources – Payload 1 Mode

## Slide 84: Communications: Data Sources – Payload 2 Mode

## Slide 85: Communications Throughput Budget
Each of the previous 5 modes are mutually exclusive
The most data intense mode, at 9600 baud, 1.5 minutes of downlink time will be needed per day

## Slide 86: Command and Data Handling (C&DH) Sub-system

## Slide 87: Papers
• TS-7600 Specs: https://wiki.embeddedarm.com/wiki/TS-7600
•Programming Language: https://www.activestate.com/blog/2016/09/python-vs-cc-embedded-systems
•Triple Modular Redundancy: https://www.isa.org/standards-and-publications/isa-publications/intech-magazine/2003/october/more-is-always-better-when-its-critical/

## Slide 88: C&DH Architecture

## Slide 89: Programming Language: Selection Process
PYTHON | C
High-level language; requires Hardware Abstraction Layer (HAL) to interface with embedded system; removes overhead | Mid/low level language; can be customized to work with any hardware out of the box (access memory registers directly using pointers)
Simpler language, readable; often faster creation time | Harder to read; often longer creation time
Slower runtime | Compact file sizes & faster runtime
No HAL available for the TS-7600; would require more code and time | Sample code for the TS-7600 is provided in C
Dynamically interpreted: more likely errors will occur during compilation | Statically interpreted

## Slide 90: Software Architecture

## Slide 91: Uplinked Commands
Command library – one file for each command

## Slide 92: Onboard Computer (TS-7600)
CPU | ARM, 454 MHz
RAM | 256 MB
Storage | 8 MB (Onboard), 2 microSD Sockets
Data Acquisition & Control | 55 Digital IO, 4 ADC pins
Interfaces | 10/100 Ethernet 2x USB 8x Serial/COM ports 1x SPI 1x I2C 1x CAN
Onboard Devices | RTC, WDT, Temp. Sensor
Operation Temperature | -20 °C to 70 °C
Power Consumption & Supply Voltage | 1.20 W (Max), 5 VDC (OP)
Size | 74 mm x 66 mm

## Slide 93: Assembly, Integration, and Test (AI&T)

## Slide 94: Mechanical
*Shaker table at Queens available.
**Vacuum chamber at RMC to be used.
Test | Description | Involved Subsystems | Start Date | End Date
Deployment | Ensure TS-7600 and EPS power on when switch is released; Test TS-7600 timer prior to antenna deployment | TS-7600, EPS | Oct-2017 | Dec-2017
Vibration Testing* | Simulate launch sequence natural modules with vibration table | Primary and Secondary Structure | Oct-2017 | Dec-2017
Thermal Vacuum Testing** | Operate basic functions in vacuum and low/high temperatures-depending on securing sufficient chamber | All | Mar-2018 | April-2018

## Slide 95: Electrical - Power
Test
Description
Involved
Subsystems
Start Date
End Date
Solar Panel PCB
Design and Testing
Eagle
Software to develop
integration to structure and
EPS
Structure,
EPS, LEDs
Oct-2017
Feb-2018
PCB Outgas Test and Electrical Performance
Place PCBs in vacuum
chamber (IGPR),
measure
mass before and after
EPS
Jan-2018
Feb-2018
Output Power
Consumption data
Ensure power consumption
data can be output and
recorded
All
Oct-2017
Dec-2017
Battery Curves
Experimentally verify
battery cycle
curves,
charge/discharge
rates
EPS
Jan-2018
Feb-2018

## Slide 96: Electrical – ACDS / Telemetry
Test | Description | Involved Subsystems | Start Date | End Date
Hysteresis Rod/Magnet Test | Experimentally verify decay rates of tumbling in Helmholtz coil | Hysteresis material, Permanent magnets | Oct-2017 | Nov-2017
Solar Cell Attitude Determination | Verify solar cells can identify pointing direction | EPS, TS-7600, Solar Array | Feb-2018 | Feb-2018
Calibration | Ensure measurement systems correlate with data sheets (magnetometer, gyroscope, thermocouples) | TS-7600, Telemetry sensors | Oct-2017 | Nov-2017
Telemetry | Use OBC to collect analog data through ADC | All | Jan-2018 | Mar-2018

## Slide 97: Electrical – Communications / CDH
Test | Description | Involved Subsystems | Start Date | End Date
Antenna Release Mechanism | Verify burn wires capable of releasing antenna array upon deployment | TS-7600, Antenna array, Structure | Oct-2017 | Dec-2017
Dummy Load Testing | Simulate sending of telemetry via transceiver without broadcasting of signal | Transceiver, Dummy antenna | Oct-2017 | Nov-2017
File Transfers | Package, transmit data to and from communication board | TS-7600, Comms | Nov-2017 | Dec-2017
Real-Time Clock | Gather data at given time intervals to validate reliability of RTC | TS-7600, Spectrometer | Oct-2017 | Nov-2017
Watchdog Timer | Ensure that the Watchdog Timer will reset the computer after a malfunction | TS-7600, EPS | Nov-2017 | Dec-2017
Operating Modes | Cycle through operating modes and ensure subsystems are capable of communicating with and being controlled by the CDH board | All | Jan-2018 | Feb-2018

## Slide 98: LEDSAT
Test | Description | Involved Subsystems | Start Date | End Date
Wavelength Testing | Ensure LED wavelength can be measured using double-blind test | Arduino, LED Array | Oct-2017 | Nov-2017
Mode A Preliminary Testing | Use Arduino to alternate between LEDs on each panel | Arduino, LED Array | Oct-2017 | Oct-2017
Mode B Preliminary Testing | Use Arduino to transmit Morse code | Arduino, LED Array | Oct-2017 | Oct-2017
Mode A Testing | Alternate LEDs between panels and wavelength using TS-7600 | TS-7600, LED Array | Nov-2017 | Dec-2017
Mode B Testing | Use TS-7600 to transmit Morse code | TS-7600, LED Array | Nov-2017 | Dec-2017
PCB Testing | Basic functionality after PCB mounting | LED Array | Nov-2017 | Dec-2017
LED Power Draw | Ensure power consumption is within expected values | LED Array, EPS | Oct-2017 | Oct-2017

## Slide 99: Spectrometer
Test | Description | Involved Subsystems | Start Date | End Date
Calibration | Ensure spectra when taken matches experimentally verified data. Calibrate light sensor criteria | Spectrometer and Optics, TS-7600 | Oct-2017 | Dec-2017
Take Spectra & Reconstruct Data | Take spectra and able to recreate the ADU spectra from raw spectrometer data | Spectrometer and Optics, TS-7600 | Oct-2017 | Dec-2017
Repeatability | Determine typical variance in spectra under constant conditions | Spectrometer and Optics, TS-7600 | Dec-2017 | Jan-2018
Specular Illumination Lobe | Determine angular lobe for each sample initially | Bédard's Goniometer experimental set-up | Nov-2017 | Dec-2018
Model SED of Lamp | Construct a before and after irradiation SED of a QTH10B bulb | “” | Oct-2017 | Oct-2017
Spectral Collection Parameters | Determine optimal integration time - large enough to differentiate from noise, small enough to not saturate detector | Spectrometer and Optics, TS-7600 | Oct-2017 | Nov-2017
Build and Integrate Baffles and Iris | Create a point source. Will also need to collect this light source as the "true representation" of our light in the optical system | Structure | Nov-2017 | Dec-2018

## Slide 100: Initialization Sequence
Test | Description | Involved Subsystems
Deployment | Release of rail switch boots EPS, initialization of TS-7600, antenna deployment | Structure, EPS, TS-7600, Antenna
LEDSat Beacon | Upon collection of sufficient power from solar array, begin LEDSat beacon (dependent on current bus status) until comms have been established | Solar Array, EPS, LED Array, TS-7600
Telemetry | Collect and save telemetry at specified frequencies, broadcast presence over communications system | Telemetry sensors, TS-7600, Communications, EPS
Handshake | Establish data link between ground station and satellite | TS-7600, Communications, EPS
Run COSMOSat | After communications have been established, permission is granted to gather and save spectra based on orbital position/desired frequency | Spectrometer, optics, TS-7600, EPS
Payload continuation | Collection of scientific data from COSMOSAT, upload settings for Mode B of LEDSAT | LED Array, TS-7600, EPS

## Slide 101: Programme Management

## Slide 102: Program Schedule
Critical Path

## Slide 103: Program Budget - Hardware
Communications | Transceiver | Budgeted | NanoAvionics | $6,744.47
 | Dummy Load | Budgeted | Mouser | $91.07
 | Antenna | Budgeted | NanoAvionics | $4,153.88
EPS | Power Distribution System | Budgeted | NanoAvionics | $4,984.43
 | PCBs | Budgeted/Estimated | AP Circuits | $877.28
 | Solar Cells | Actual | Azur | 8081.71
Thermal | Multi-Layer Insulation | Actual | Dunmore | $700.60
 | Heater Design Kit | Actual | Minco | $277.98
Structure | Aluminum 7075 T6 | Budgeted | McMaster-Carr | $512.00
 | Hardware | Estimated |  | $50.00
 | Deployment Springs | Estimated |  | $56.50
 | Deployment Switches | Estimated |  | $113.00
Telemetry | Thermistor | Estimated |  | $204.48
ADCS | Magnetometer | Budgeted | Elmwood Electronics | $56.16
 | Gyroscope | Budgeted | Sparkfun | $80.44
 | Magnetic Rods | Budgeted |  | $45.00
 | Hysteresis Rods | Budgeted |  | $150.00
OBC | External ADC | Budgeted | TI | $41.89
Spectrometer | Silver Coated 1/2" Off-axis parabolic mirror | Budgeted | Thorlabs | $223.58
 | Collimation Lens | Budgeted | Thorlabs | $63.77
 | 90 degree Collimation Lens | Budgeted | Avantes | $573.75
 | Payload Segregation Wall | Estimated | In-house | $0.00
 | Custom Lamp Holder Cap | Estimated | In-house | $0.00
 | Sample Stage | Estimated | In-house | $0.00
LEDSAT | Green LEDs | Budgeted | Mouser | $107.24
 | Red LEDs | Budgeted | Mouser | $99.89
 |  |  | TOTAL | $29,226.83

## Slide 104: Program Budget – Other Costs
Structure | Machining | Primary and Secondary Structure Fabrication | Queens University | $40.00 | 15 | $0.00 | $0.00 | 1 | $600.00
 | Hard Anodizing | Four Type III hard-anodized Al 7075-T6 Rails | Waterloo Electroplating | $90.00 | 1 | $0.00 | $0.00 | 1 | $90.00
ADCS | Solar Panel Attitude Determination | Required: 3D printed mount and Arduino DAQ |  | $90.00 | 1 | $0.00 | $0.00 | 1 | $90.00
 | PSD and pin-hole testing | Required: aluminum pin-hole structure |  | $0.00 | 1 | $0.00 | $0.00 | 1 | $0.00
 | Magnetic/Hysteresis Rod Testing | Large aluminum frame, copper coils for Helmholtz coil, fidget spinners |  | $0.00 | 1 | $0.00 | $0.00 | 1 | $0.00
EPS | Battery Testing | 18650 Li-ion battery testing | Elmwood Electronics | $9.99 | 5 | $10.00 | $0.00 | 1.13 | $66.44
Hardware/Wiring |  | Estimated |  | $601.46 | 1 | $0.00 | $0.00 | 1 | $601.46
 |  |  |  |  |  |  |  | TOTAL | $1,447.90

## Slide 105: Program Budget – Project Income
Based on last year
Dean's Donation (fall 2016) | $15,000.00 | October-24-16
QYEA cheque | $2,135.00 | November-04-16
Student Activity Fees (90%) | $7,702.71 | November-09-16
Sponsorship Cheques - Aversan and Thorlabs | $1,000.00 | November-20-16
Sponsorship Cheques - MDA | $500.00 | December-03-16
Shell Activity Fund | $5,000.00 | December-03-16
QYEA cheque | $1,000.00 | March-09-17
Dean's Donation (winter 2017) | $15,000.00 | March-17-17
Sponsorship cheque | $2,000.00 | March-21-17
Sponsorship Cheque- GASSI | $5,000.00 | March-24-17
Student Activity Fees (10%) | $829.36 | April-21-17
Shell Activity Fund | $5,000.00 | May-11-17
TOTAL | $60,167.07 | 

## Slide 106: Project Risk Management
Team Dynamics
  QSET is an open-access team
  Potential difficulties in ensuring deadlines are met
Knowledge gap
  First time @ CSDC
  Significant time spent in learning curve
    Mitigation using wiki and through mentorship culture of team
Facility and Equipment Access
  Highly dependent on partnership with professors at Queen’s University and Royal Military College for lab usage
OBC development
  Critical path in development

## Slide 107: Payload Risk Management Analysis at PDR
Failure Mode | Cause | Mitigation Method
Spectrometer Damage | Dislodge at launch Debris impact Radiation Vibration misalignment Thermal | Shielding AvaSpec Mini used in environmental research (ruggedized for vibration)
Degradation of Optics | Radiation | Shielding, sample redundancy, reference sample
Dislodged Optics | Vibration Thermal | Plate-mounted lenses, sample Redundancy
Notes: Degradation of Optics: Space Radiation (Potential Loss of Signal through optical assembly)
Dislodged Optics: Dislodge from launch, Vibrations from orbit, Impact from Debris
  POSSIBLE OTHERS THAT DON’T FALL UNDER “DAMAGE”: Changes to internal gratings due to temperature fluctuations

## Slide 108: Updated Payload Risk Management Analysis
Mode | Effect | Mitigation
Vibration | Optics misalignment Detachment of mounts | Monolithic design reduces components and limits movement Low-outgas epoxies to secure components
Thermal | Thermal warping Detector noise | Metal components have matched thermal expansion Low-expansion fused silica optics Temp. sensor check prior to payload
Radiation | Burnout of CMOS Detector drift | Free-space optics reduces degradable components CMOS detector less susceptible than CCD to charge buildup
Light | Burnout of CMOS | Operation in eclipse On-board lighting
Power | Unable to complete task | EPS
Comms | Unable to transmit Data corruption | Payload 2 system Parity bit check

## Slide 109: Mitigation of Payload Error
Noise | Effect | Mitigation
Radiation | Changing light SED Degradation of optics and spectrometer Corruption of data | Reference lamp and background sampling Enclosed design reduces exposure CDR testing to quantify effects Record multiple spectra per test Triple modular redundancy in storage
Stray Light | Noise in CMOS | On-board lighting Operation in eclipse Record background @ test
Thermal | Noise in CMOS Aberrations | Operation only during narrow temperature range Record temperature @ test
Light Stability | Noise in CMOS Changing light SED | Let lamp equilibrate before sampling Vacuum chamber and CDR tests to quantify effects Record multiple spectra per test

## Slide 110: Concept of Operations (CONOPS)

## Slide 111: Concept of Operations: Overview

## Slide 112: Concept of Operations: LEOP and Default Mode

## Slide 113: Concept of Operations: Payload 1

## Slide 114: Concept of Operations: Payload 1

## Slide 115: Concept of Operations: Payload 2

## Slide 116: Concept of Operations: Payload 2

## Slide 117: Concept of Operations: Payload 2A
Satellite is tumbling
LEDs of given wavelength on each panel are held on for 20 s, then switch to the next panel
+x panel
+y panel
-x panel
-y panel
Command
Wait 20 sec
Command
red
red
red
red
green
green
green
green

## Slide 118: Concept of Operations: Payload 2B
Satellite has stabilized
  [-z] points within of Kingston while overhead
Morse code message, which was uplinked, is transmitted using selected LEDs

## Slide 119: Concept of Operations: Nominal Timeline
LEOP
Mode | Event Name | 0:00 |  | 0:30 |  | 1:00 |  | …. | 3:00 |  | 3:30 |  | …. | 8:00 |  | 8:30 |  | 9:00 |  | 9:30 | 
Deployment | Deployed |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Power On |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Read/Record Time and Boot Count |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Deploy Antenna |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Default Mode | Query Receiver |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Transmit Telemetry |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Uplink: Enter Communications Mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Communications Mode | Access Telemetry |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Uplink: Command Continous transmission |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Transmit Data (1 Hz) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Enter Default Mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Ground Ops: Check sensor calibration, satellite orientation, satellite health |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Default Mode | Query Receiver |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Transmit Telemetry |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Uplink: Enter Communications Mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Communications Mode | Access Telemetry |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Uplink: Command Continuous Transmission |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Transmit Data (1 Hz) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Enter Default Mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Ground Ops: Check sensor calibration, satellite orientation, satellite health |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Default Mode | Query Receiver |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Transmit Telemetry |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Uplink: Enter Communications Mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Communications Mode | Access Telemetry |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Uplink: Enter Payload 2A Mode in 95 min. Green LEDs, contact time of 7 minutes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Ground Ops: Check telemetry, prepare telescopes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 120: Concept of Operations: Nominal Timeline
Mode | Event Name | 8:30 |  | 9:00 |  | 9:30 |  | 10:00 |  | 10:30 |  | 11:00 |  | 11:30 |  | 12:00 |  | ….. | 19:00 |  | 19:30 |  | … | 21:00 |  | 21:30 | 
Default Mode | Query Receiver |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Transmit Telemetry |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Enter Payload 2A Mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Payload 2A Mode | Verify satellite is in eclipse and power capacity is sufficient |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Alternate through green LEDs |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Ground Ops: SSM or TRM tracking of LEDs using filter & CCD |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Default | Query Receiver |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Transmit Telemetry |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Uplink: Enter Communications Mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Communications Mode | Access Telemetry |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Uplink: Enter Payload 1 Mode 5 orbits from now |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Downlink LED data. Ground Ops: Check LED power consumption, correlate to brightness |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Default Mode | Query Receiver |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Transmit Telemetry |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Enter Payload 1 Mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Payload 1 Mode | Verify satellite stray light is below threshold and power is sufficient |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Activate lamp, take spectra, store data, power off |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Enter Default Mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Default Mode | Query Receiver |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Downlink telemetry and science data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCIENCE MODES

## Slide 121: Payload #1: Sources of Error

## Slide 122: Concept of Operations: Payload Anomalies
Mode | Detection | Response
Misalignment of optics | Significant decrease in light throughput | Continue operation on remaining samples Attempt sampling in sunlight
Thermal warping | Spectral drift Temp. measurements | Tighten thermal constraints Post-processing correction
Stray light | Unexpected spectral features Increased noise floor Background spectra Sun sensors | Tighten ambient light constraints Post-processing correction
Detector response drift | Reference and background spectra | Post-processing correction Allow time for passive discharge if possible
Optical aberrations | Ghost images in spectrometer Decreased light throughput | Post-processing correction

## Slide 123: Concept of Operations: Payload Anomalies (cont.)
Mode | Detection | Response
CMOS noise | Inconsistent unexpected spectral feature Drift | Increased sampling Post processing correction
Unable to transmit | No data received Timeout No 'data received' signal | Re-attempt on next cycle
Internal comms. noise | Increased data noise floor | Triple modular redundancy Manual filtering on ground
Burnout of CMOS | No spectral data | Re-attempt on next cycle
Power failure | EPS query | Re-attempt on next cycle
Data corruption | Triple modular redundancy error log | Increase sampling rate Adjust orbit location during sampling to avoid radiation hotspots

## Slide 124: Concept of Operations: CDH Anomalies
Mode | Detection | Response
Single event latch-up | Watchdog timer fails to reset | Timeout signal is sent to initiate power cycle (WDT)
Unable to transmit | Timeout No 'data received’ signal | Re-attempt on next cycle
Internal comms. noise | Increased data noise | Triple modular redundancy
Power failure | Watchdog timeout signal | Initiate power cycle

## Slide 125: Concept of Operations: CDH Anomalies
Mode | Detection | Response
Data corruption | Triple modular redundancy error log | Flag data files with multiple errors to inspect Send these data files to earth If needed, can use system restore command to go back to a previous state; second duplicate SD card will also have the OS installed (RAID1)
Out of memory storage | Unable to save files OS will detect this | Dump old data to earth on next comms window
Program not responding | Timeout | Timeout signal sent to restart program; re attempt process on next cycle

## Slide 126: Educational Outreach

## Slide 127: Science Quest (SQ) – March 2017
Summer & school-year camp with gr. 1 – 8 students in Kingston, with ~20 campers in each group.
QSET has done workshops with SQ over the last few years with their various camp programs
Notes: https://sciencequest.ca/clubs-photos-2016-2017/
Please summarise the Educational Outreach presentations you have given
  Locations, approximate number of people, any local media coverage

## Slide 128: Science Rendezvous (Kingston) – May 2017
Science Rendezvous is an annual Canada-wide event bringing people in STEM fields to present in their communities
QSET presented their decade of work in space-related technologies to hundreds of students and families in the Kingston area.
Local media and Science Rendezvous organizers were present at the event

## Slide 129: Other Outreach
Orientation week showcase on Queen’s campus to ~700 first-year engineering students Sept. 2016 and 2017
Presented to representatives from GM during a design team visit in the fall 2016
High school students toured our workspace where we displayed our ongoing projects
Showcased work at the 2016 Queen’s Space Conference to ~150 attendees and presenters
Publicly documents all team work on QSET webpages (www.qset.ca and qsat.wikidot.com)

## Slide 130: Summary

## Slide 131: Summary – Accomplishments
General
  Partnered with RMC for ground station access
Payloads
  Incorporation of multiple payload capabilities
    Payload 1: Collection of spectral BDRF of three samples and one reference
    Payload 2: LED visual communication on satellite exterior
  Robust design allows functionality under broad conditions
Structure & Thermal
  CAD model ready for prototyping
  Models predict viable thermal operation and vibrational integrity
  Overall 3.9 kg mass (incl. margin)

## Slide 132: Summary – Accomplishments (cont.)
Power & Communications
  Designed EPS system to handle power requirements of payload
ADCS & CDH
  Passive ADC system greatly simplifies overall satellite controls
  CDH architecture can identify and correct single-bit flips
  Designed and currently testing data transfer, error detection and handling, and watchdog systems
Outreach
  Wide variety of outreach projects, building relationships with local schools and camps to provide educational workshops
  Plans to continue relationship with ScienceQuest, Science Rendezvous, and the Engineering Society of Queen’s University

## Slide 133: Summary – Next Steps and Required Assistance
Overall
  Test initialization procedure
  Access to vacuum chamber; no facility for thermal testing
  Management of risk in team dynamics
  Shift from design phase into system construction and testing
Payload
  Simulate lab results
  Calibration and post-processing procedure
  Morse code transmission with LED
Structure & Thermal
  Battery heating/lamp cooling tests
  Manufacture and prototype to confirm models
Notes: Why we are ready for the next stage of development?
This is our team’s first year in this competition – although we have limited physical construction as of this date, our focus on robustness in design allows us to save time down the line and assemble/test our systems in time for the April final thermal vacuum/vibration testing

## Slide 134: Summary – Next Steps and Required Assistance
Power & Communications
  Design solar panel PCB & test outgassing
  Determine battery cycle curves & confirm power usage
ADCS
  Model sun sensing capabilities
  Test tumbling decay rates in Helmholtz cage
  Calibration
CDH
  Dummy load testing
  Ensure watchdog and error-correction functionality

## Slide 135: Supplementary Information

## Slide 136: Testing Objectives and Outcomes @ CDR
Collect SED of lamps before and after irradiation
  Observe changes in SED, equilibration time, power, stability
Collect three reference spectra prior to irradiation, and again periodically during and after irradiation.
  Observe changes in spectral shape and noise
Send text file with known data every 10 seconds, for an hour
  Compare text files stored on irradiated CPU with file on PC
Exp. | Component | Testing Outcomes
1 | Quartz Tungsten Halogen Lamp | Observe changes in SED due to time based radiation
2 | Spectrometer | Observe changes in spectral response of the CMOS detector
3 | Onboard Computer | Observe changes in data transferred between computers
Notes: Will determine what the lifetime of the bulb is when exposed to radiation: Good to know to get an idea of how many spectra we would be able to take
Data processing models assume a stable light source: Good to know if a “stable’ light source can be approximated
  Spectral BRDF is a ratio therefore I don’t think it matters if the intensity of the light source changes???? Bigger deal if we want to track kinetics based on a spectral feature
  Will provide integration times that are acceptable (I don’t think it matters what the integration time for BRDF) but would matter if we want to track kinetics based on a spectral feature
Spectrometer
Indicates any changes in spectral response: detector may become less/more sensitive to different wavelengths therefore some correction parameters may be necessary
2. Check on radiation+CMOS effects some more
1. Radiating the spectrometer
Ask James if there are any materials that we would be able to test to get an idea of how long it takes to see a noticeable change.

## Slide 137: Payload 1 Background and Theory

## Slide 138: Space Environment Material Degradation Experiments
VIS-NIR reflectance spectroscopy has been used to identify asteroid composition [P4]
Payload extends research by Bedard et al. to create a database of spacecraft material reflectance spectra [P4]
Material reflectance properties will change as they are bombarded in space [P1, P2, P4]

## Slide 139: Data Collection in Ground-Based Experiments
As surface roughness increases the specular spike decreases
(specular-diffuse lobe increases) [P5]

## Slide 140: Bi-directional Reflectance Distribution Function (BRDF)
BRDF model reflectance as a function of illumination geometry and wavelength [P2]
Materials exhibit unique BRDF based on surface structure, composition, and roughness [P2]
Time-series data collected will be used to extend existing models
Colour ratios of filtered spectra may also be used to classify materials [P2]
Notes: Spectral bidirectional reflectance distribution [sr-1] Measured reflectance signal [ADU]
Measured incident signal [ADU]
Exposure time [s]
: Exposure time of reference signal [s]
Solid angle of the detector [sr]
: Incident angle [degrees]
Reflected angle [degrees]
𝑓_𝑟 (𝜃_𝑖, 𝜃_𝑟, 𝜆): Spectral bidirectional reflectance distribution [sr-1] 𝑆_𝑟 (𝐸_𝑖, 𝜃_𝑖,𝜃_𝑟, 𝜆): Measured reflectance signal [ADU]
𝑆_0 (𝜆), Measured incident signal [ADU]
𝑡_(exp(𝑟)): Exposure time [s]
𝑡_exp⁡(0) : Exposure time of reference signal [s]
∆𝜔_𝑠: Solid angle of the detector [sr]
𝜃_𝑖: Incident angle [degrees]
𝜃_𝑟: Reflected angle [degrees]

## Slide 141: Bi-directional Reflectance Distribution Function (BRDF)
BRDFs identify surface roughness through:
Reddening Effect
  Increase in intensity of reflected red wavelengths [P1, P2]
Slope of the BRDF
  Identified as a parameter that may be used to model orbital age [P1, P2]

## Slide 142: Payload 1 Instrumentation and Design

## Slide 143: CMOS Spectrometer (Avantes Ava-Spec Mini) [P3]
Selected for its light weight and small size
CMOS detector was selected over CCD variants due to less susceptibility to electron buildup on detector surface
Physical Specs. |  | Perform. Spec. | 
Weight | 174 g | Range | 200 – 1100 nm
Size | 9.5 x 2 x 6.5 cm3 | Resolution | 2.35 nm
Operating Temp. | 0 – 55 oC | Connection | USB 2.0
Grating | 300 line/mm | Blaze | 300 nm

## Slide 144: Quartz Tungsten Halogen Lamp (Thorlabs QTH10B) [P6]
Better output stability and more uniform spectral distribution over similar xenon-arc lamps
10W input power (@ 12 VDC)
400 – 2000 nm useful range
Must be cooled to prevent burn-out (i.e. conduction tape)
Notes: Thorlabs Inc., “Quartz Tungsten-Halogen Lamp.” Thorlabs Inc., 2017.

## Slide 145: Optical System Design
Design Element | Justification
Single observation angle at 60o incident/reflection | Maximum exposure of sample with minimum instrument exposure, while matching existing data Specular reflection provides most light for measurements
Free-space optics | Reduces degrade-able components and complexity
Samples housed inside exposed via slot | Protects sensitive instrumentation and removes need for moving deployment rigs
On-board lighting | Reduces attitude control needs and improves consistency as LEO orbits have rapid illumination geometry change Sunlight may be used as a back-up, opening possibility of additional illumination geometries

## Slide 146: Payload 2 Background and Theory

## Slide 147: Payload 2: Inverse-Square Law
Inverse-Square Law for an LED in orbit:

## Slide 148: Payload 2: LED Magnitude

## Slide 149: Payload 2: Luminous Efficacy of Radiation
Converting lumens (luminous flux) to Watts (radiant flux)
  Must use this to specific power output from commercially-available LEDs
Source: http://www.ledsmagazine.com/articles/2005/05/metrics-for-solid-state-lighting.html

## Slide 150: Payload 2: Trade Study
Trade-off between radiant flux and beam FWHM

## Slide 151: Payload 2: LED Selection
Wavelength
  Green provides best visibility to human eye
  Red provides high power and atmospheric penetration efficiency
Green LEDs:
Red LEDs:

## Slide 152: Payload 2: LED Beam Pattern

## Slide 153: Payload 2: STK Simulations
Assumed stabilized with LEDs nadir pointing
Access calculated over year-long space assuming ISS orbit, and that LEDs are only visible during eclipse
Notes: - Large gaps due to offset in CoSMOSAT’s orbit time and the Earth’s rotation

## Slide 154: Payload 2: Contact Times
January-February
July-August
Average Contacts per Day | 2.05
Average Total Contact time per Day | 276 sec
Average Time per Contact | 138 sec
Contact Period Length | 41 Days
Average Contacts per Day | 1.07
Average Total Contact time per Day | 111 sec
Average Time per Contact | 109 sec
Contact Period Length | 34 days